UT1001 The Ultimate Overdrive 1928-1931 is

a unique, fully synchronized, transmission for the Model "A". The overdrive is built inside the case. There are no extra levers, cables, or electric switches involved.

The 22% overdrive feature allows you to drive a stock Ford Model "A" at the highway speeds of 50-55MPH without over revving your engine. It will not bog down like the 33% drive line units.

The Drop In Conversion Kit (provided) has all parts (clutch, pressure plate, transmission assembly, pedal brackets, drive shaft, torque tube, radius rods, etc.) necessary for a drop in installation. No special tools are required. the only thing that you need to buy is oil for the transmission and rear end. We must have a useable torque tube, drive shaft, and radius rods to do your conversion. If you wish to do this on an exchange basis, please add $125 deposit, which will be refunded in full when you return these parts. D&J Manufacturing will pay the shipping on the parts you return.

The gearshift lever is a chrome finish. It uses the side mount emergency brake lever (30-31). Because the tower moves back about one and one half inches, the floorboard needs to be trimmed.

Shipping is by UPS freight. The shipment is a minimum weight of 250 pounds and may run a few pounds over. You may call your local UPS office for a quote. Please use Zip Code 95046 for a reference.

The price is $3,200.00 F.O.B. San Martin, Ca. 95046. California residents add sales tax. Please allow 6 - 10 weeks for delivery.

There is a crating fee of $45.00 for the two wooden crates for the shipping of the transmission and the drive train.

One other thing to think about is if you replace a clutch assembly it will cost about $100. Rebuilding a transmission $400 to $500 to do it correctly. The tower will run $50 to $100 if you rebuild the forks. A U-Joint now costs close to $100 and any of the overdrives run $800 to $1,800. If you add this all up you have from $1,450 to $2,600 invested and you still have the old Model "A" Transmission. Remember that all you need to do is save one engine and it pays for itself.

Full Customer Satisfaction Guaranteed by D&J Manufacturing.

Don't settle for less!